## Slide 1: Design Notes for 128-channel Headstage Motherboard
Doug Weber
5/16/2021

## Slide 2: Concept
128-channels of HDEMG split across 4 flexPCB sub-arrays, each containing 32-channels
“Motherboard” containing:
  Connectors that mate with the Intan headstage electronics
  4 ZIF-style edge connectors that mate with the sub-arrays
Motherboard
Intan 128-ch headstage

## Slide 3: Rough layout
Intan Headstage connectors:
2x Molex SlimStack 502426-6410
(16.1 mm x 2.6 mm)
Intan 128 channel headstage
32-channel ZIF edge connectors
Channels 0-31
Channels 32-63
Channels 96-127
Channels 64-95
NOTE: This layout is completely arbitrary. Routing the traces may be difficult, and it may be better to position the edge connectors differently to make it easier to route the traces from the Intan headstage connectors to the ZIF connectors.

## Slide 4: Vendors
Mouser electronics
  60 x Molex SlimStack Connectors